## Slide 1: The Power of Physics Estimation… …in sorting out future options
Tom Murphy
UCSD Physics

## Slide 2: Inspired By…
Famous physicists like Fermi and Feynman frequently formulated fantastic feats of estimation
  optional: “estimation”  “finagling figures”
Best course I ever took: Order of Magnitude Physics at Caltech
  team-taught by Peter Goldreich and Sterl Phinney
Estimation and Scaling in Physics (UCSD Phys 239)
  team-taught by Fuller, Diamond, Murphy spring 2010, 2012, 2014

## Slide 3: Our Trajectory Today
Fermi Problems
Climate Change
Limits to Growth
Fossil Fuel Replacements?
Energy Storage
Fuel Economy of Cars and EV Math

## Slide 4: Color Coding to Clarify
Black: generic/default
Orange-brown italics: emphasis
Red: assumptions
Blue: constants/knowledge
Purple: results
A note on numbers:
  math is a lot easier if you don’t take numbers so seriously
  π = 3 = sqrt(10) = 10/3
  2 ≠ 3, but 8 ≈ 9
  c, e, h, kB, mp, me, σ, G, NA, μ0, ε0, RE, ME, rAU, etc. by memory

## Slide 5: Fermi Problems
How many piano tuners in Chicago?
How many molecules from Julius Caesar’s last breath do you draw in with each breath?
How far does a car travel before a one-molecule layer is worn from the tire?
How many laser pointers would it take to visibly illuminate the Moon?
How heavy is a typical cloud?
Book: Guesstimation (by Weinstein and Adam)
  plus second volume by Weinstein

## Slide 6: Example Fermi Problem
How many kids are laughing so hard right now that milk (or cultural equivalent) is streaming out of their noses?
7 billion people in the world
Life expectancy: 60 years
Vulnerable age: 4 to 10  10% of life  700 million at risk
Half of adults have had this experience  350 M at risk
Once-in-lifetime event, 5 sec duration  5/(6×π×107)
350 M × 0.3×10−7 ≈ 10

## Slide 7: Our Trajectory Today
Fermi Problems
Climate Change
Limits to Growth
Fossil Fuel Replacements?
Energy Storage
Fuel Economy of Cars and EV Math

## Slide 8: The Rise of CO2
Charles Keeling (SIO/UCSD), started measuring atmospheric CO2 from Mauna Loa in
Hawaii in 1958. Besides the annual photosynthetic cycle, a profound trend is seen.
400 ppm = 400 parts-per-million = 0.04% by volume
2 ppm/yr
reference

## Slide 9: Is this Rise Surprising?
Every gram of fossil fuel used produces 3 grams of CO2
  it’s straight chemistry: to get the energy out via combustion, the carbon from the hydrocarbon gets attached to oxygen and off it goes
How much should we expect?
  global energy budget is 41020 J/yr from fossil fuels (51020 J/yr total)
  average 10 kcal/gram  ~40,000 J/gram  1016 g/yr F.F.
  so 31016 g/yr CO2  31013 kg/yr CO2
  atmosphere has mass = 51018 kg  CO2 adds 6 ppm/yr by mass
  about 4 ppm/yr by volume (CO2 is 44 g/mol vs. 29 for air)
  50/50 to ocean/atmosphere, atmospheric rise is 2 ppm/yr, by volume
  this is darned close to what we see on the “Keeling curve” graph

## Slide 10: Total CO2 Rise
We can do the same thing for the entire fossil fuel history
  have gone through 1.2 trillion barrels of oil  170 Gtoe
    Gtoe is gigaton (109 ton) oil equivalent (by energy)
  used about 180 Gtoe coal worldwide
    using 45 Gtoe U.S. times four, since U.S. uses ~25% of world energy
  used 1100 tcf natural gas in U.S.  30 Gtoe, so guess 120 Gtoe worldwide
  470 Gtoe of fossil fuels  1.41015 kg of CO2 (3 FF mass)
  280 ppm of atmosphere by mass; 180 ppm by volume
  half into atmosphere  90 ppm increase
  see 115 ppm increase (280 ppm pre-industrial to 395 ppm today)
So the CO2 increase is absolutely expected!

## Slide 11: Expected Temperature Rise
Applying σT4 in radiative equilibrium, Earth is 255 K
  but actual number is 288 K, thanks to 33 K greenhouse effect
If you add to the blanket, expect to get warmer
How much warmer?
  we know that 7C of the 33°C greenhouse effect is from CO2
  have gone from 280 to 385 ppm (11/8 times as much, or 3/8 increase)
  “dumb” proportionality translates into 73/8 = 21/8 = 2.6C change
    but takes some time because oceans are slow to respond, having enormous heat capacity
    actual logarithmic nature approximately linear for small changes
Should be NO SURPRISE that burning loads of fossil fuels makes us warmer
  not actually hard to understand!

## Slide 12: Our Trajectory Today
Fermi Problems
Climate Change
Limits to Growth
Fossil Fuel Replacements?
Energy Storage
Fuel Economy of Cars and EV Math

## Slide 13: Exponential Estimations
Sum of all forms of energy used in the U.S. (fossil fuels, nuclear, hydro, wood, etc.)
Red curve is exponential at 2.9% per year growth rate
World is at 16 TW now; pick 2.3% rate, mapping to 10× per 100 yrs.
logarithmic plot of the same
1650
1650
2050
2050

## Slide 14: Extrapolating at 10× per Century
power output of sun
1340 years
power output of the entire Milky Way galaxy
~2500 years
405 yr
solar power reaching Earth’s upper atmosphere
320 yr
solar power reaching Earth’s land
all solar
land
16 TW today
(1.6×1013)

## Slide 15: Waste Heat Boils Planet (not Global Warming)
body temperature
water boils
paper burns
steel melts
sun surface temperature
global warming?
thermodynamic consequence of
arbitrary energy technology on Earth
Straightforward application of σT4 radiative disposal of heat: only ticket off planet

## Slide 16: Physics Predicts an End to Economic Growth
Physical growth (energy, population, etc.) on finite Earth is clearly limited
Physical resources will always be an important component of economic activity (never below 10%, for instance?)
Cap in physical growth means cap in economic growth
  Growth is a transitory phase, so major adjustments ahead
Fossil Fuel trajectory is set: growth during ascent; what next??
we are here

## Slide 17: Our Trajectory Today
Fermi Problems
Climate Change
Limits to Growth
Fossil Fuel Replacements?
Energy Storage
Fuel Economy of Cars and EV Math

## Slide 18: Estimating Post-Fossil-Fuel Resources
Usually not that hard to put numbers/limits on resources
  precision is not the goal: sort out major and minor players
Some cute ideas quickly dispensed with numbers
  lots of distractions out there
Example: Wave Power
  1 meter high, 2 m thick, 1000 kg/m3  2000 kg per meter along wave
  raised average of 0.5 m  mgh = (2000×10×0.5) = 10,000 J per meter
    double to capture kinetic energy contribution  20,000 J
  wave every 10 seconds  2,000 W for each meter of coastline
  coastlines ring world twice (two major sets of continents)
    so about 100,000 km of (projected) coastline
  108 m of coastline times 2×103 W per meter  2×1011 W, or 0.2 TW
  about 1% of global demand if fully developed!

## Slide 19: Categorize into Long-term Abundance/Scale
Clearly Abundant:
  Solar of various flavors (including algal biofuels?)
  Breeder-type nuclear (uranium or thorium)
  One-time geothermal (unsustainable mining of heat resource)
  Ocean thermal energy
  Fusion
Intermediate (potential real player):
  Wind; Geothermal for heating; Cellulosic Biofuels; Ocean Current
Borderline (small, but relevant player):
  Hydroelectric
Niche (small beans; special locations):
  Geothermal Electricity; Tidal; Conventional Fission; Biofuels from food crops; Ocean waves

## Slide 20: Matrix of Considerations; Crude Scores
Do the Math: The Alternative Energy Matrix
mind the gap!
Host of practical considerations
blue: good (+1)
yellow: marginal/okay (0)
red: insufficient (−1)
Created for Do the Math blog
Each topic has dedicated blog page
Note that fossil fuels beat the pants off of alternatives
Spells rough adjustment ahead
Lots of electricity sources
Few transportation options

## Slide 21: Corn Ethanol or Bust
Let’s calculate how much land we need to replace oil
  an Iowa cornfield is 1.5% efficient at turning incident sunlight into stored chemical energy
  the conversion to ethanol is at best 30% efficient
    assuming 1.4:1 energy-return:energy-invested, and using corn ethanol to power farm equipment and ethanol production itself
  growing season is only part of year (say 50%)
  net is 0.23% efficient (1.5%  30%  50%)
  need 40% of 1020 J per year = 41019 J/yr to replace petroleum
  this is 1.31012 W: thus need 6×1014 W input (at 0.23%)
  350 W/m2 summer insolation, need 21012 m2, or (1,400 km)2 of land
  that’s a square 1,400 km on a side; as a lower limit

## Slide 22: What Does this Amount of Land Look Like?
We don’t have this much arable land!
And where do we grow our food?

## Slide 23: Our Trajectory Today
Fermi Problems
Climate Change
Limits to Growth
Fossil Fuel Replacements?
Energy Storage
Fuel Economy of Cars and EV Math

## Slide 24: Energy Storage
A major transition away from fossil fuels to solar, wind, etc. will require massive storage solutions
The cheapest go-to solution for stand-alone systems has been lead-acid batteries
  but national battery would be a cubic mile, and require more lead than is estimated to exist in global resources (let alone proven reserves)
We can use estimation techniques to evaluate possible solutions
  focus on home-scale solutions
  scale will be 100 kWh of storage (3 days elec. for average U.S. house)
  explore gravitational, batteries, compressed air, flywheels

## Slide 25: Gravitational Storage
Hoisting rocks or pumping tanks of water: low tech approach
A rechargeable AA battery (1.5 V, 2 A-h  3 Wh ≈ 10 kJ)
Hoisting mass on 3 m derrick: need 300 kg to match AA battery
  gravitational storage is incredibly weak
100 kWh, in menacing 10 m high water tower, needs 3600 m3
  15 meters on a side
  oops
  legal hurdles; frightened neighbors

## Slide 26: Lead-Acid Batteries
Each reaction involves a Pb atom in the anode, a PbO2 molecule in the cathode, and two electrons at 2 eV each
100 kWh (3.6×108 J) needs 1027 Pb atoms
  1700 moles; 355 kg of lead; might guess 4× realistic
  real batteries would have 1500 kg of lead (2500 kg total battery mass)
2500 kg at 2.5× density of water  1 cubic meter
  will cost $15,000, and last 3−5 years
  actually, the cheapest, most compact of the four non-fossil storage means we’re considering
For U.S. to go full solar/wind requires significant storage
  not enough lead in world resources (let alone reserves) to build for U.S.

## Slide 27: Compressed Air
Charged to 200 atm, energy is P0V0ln(Pf/P0) = 5.3P0V0
  simple integration of PdV = NkT(dV/V)
P0 = 105 Pa
Need 5.3×105V0 = 100 kWh = 3.6×108 J
  V0 = 700 m3
  Vf = 3.5 m3
  cube 1.5 meters on a side

## Slide 28: Flywheel
Solid cylinder: I = ½MR2
Edge velocity, v  ω = v/R; E = ½Iω2 = ¼Mv2
Pick edge velocity v = 300 m/s
Need 16 ton mass
At density of steel, this is 2 cubic meters
  e.g., 2 meters high; 1.2 meter diameter
  acceleration at edge; v2/R is 16,000g
  break-up: exceeds mechanical strength
  need larger, slower to be safe: 2.5 m diameter, 125 m/s
    10 m3; 80 tons  1250g
can get 25 kWh
unit 2×3 m; $100k

## Slide 29: Heck: Just Use a Generator!
Each gallon of gasoline contains 36.6 kWh of thermal energy
Home Depot generator probably 15% efficient
  seems like the rest comes out in noise!
  about 5 kWh of electricity per gallon
For 100 kWh, need 20 gallons (75 liters) of gasoline
  gasoline: 0.075 m3
  lead acid: 1.0 m3
  compressed air: 3.5 m3
  flywheel: 10 m3
  water/grav at 10 m: 3600 m3
Hard to beat fossil fuels!
  by far the cheapest, too

## Slide 30: Our Trajectory Today
Fermi Problems
Climate Change
Limits to Growth
Fossil Fuel Replacements?
Energy Storage
Fuel Economy of Cars and EV Math

## Slide 31: Is 100 MPG from Gasoline Possible?
At freeway speeds, mainly fight drag: Fd = ½ρcDAv2
  ρ = 1.2 kg/m3, cD ≈ 0.3, A ≈ 2.5 m2, v = 30 m/s
  Fd ≈ 400 N
Rolling resistance is about 0.01mg ≈ 100 N (indep. of v)
Net 500 N
A gallon of gasoline (3 kg × 10 kcal/g × 4.18 kJ/kcal) contains about 130 MJ of energy
Used at ~25% efficiency in internal combustion engine
W = F×d  d = 30 MJ / 500 N = 60 km ≈ 35 miles
100 MPG from gasoline at freeway speeds is super-hard
  need a factor of four improvement in drag piece, for instance
  even a trout-shaped car unlikely to achieve this

## Slide 32: Electric Vehicle (EV) Math
Any window sticker will confirm: 30−35 kWh of juice from the wall socket provides 100 miles of travel
  using 33.5 kWh/gallon (lower heating value)  ~100 MPG equiv.
  but if from 35% efficient fossil fuel plant, back to 35 MPG
Li-ion batteries in EVs store 0.08−0.13 kWh/kg
  so 300 mile range would require 100 kWh ,or 1000 kg of battery
Today’s EV battery cost is $500/kWh
  300 mile range costs $50,000 in battery alone (hellooo, Tesla!)
  reach gasoline cost after 500,000 miles of driving (at $4/gal, 40 MPG)
  battery will not last that long: need ~4× reduction in battery price for cost parity
    not to say price should dictate everything: other reasons to adopt EV

## Slide 33: Charging Bottleneck
Adding gasoline to tank at 6 gallons per minute:
  3.6 kWh/sec = 13 MW of power!
  two cars filling at a gas station = UCSD campus power demand!
Charge efficiency 70−80%
  other 20−30% generates heat
Try sticking 100 kWh into a battery in 10 minutes
  600 kW of power (current EVs typically accept 100−200× less)
    100 houses with A/C blasting; almost 1000 horsepower
  120 kW in heat/loss
  distributed over 6 m2 (cube 1 m on a side), 20 kW/m2
  naïvely hundreds of degrees Celsius temperature rise
    unless aggressively water-cooled: not an easy job

## Slide 34: Summary
We often know more than we think about a problem
Real world problems don’t come with tidy numbers attached
Estimation and multiple techniques often fruitful
  have to at least try to solve a problem: dig in
Straightforward exercise to expose major future challenges
  basic assumptions about growth and energy are typically wrong
Every congressperson should have an estimator on their staff
  and then actually LISTEN to them!